Dimensions of Miscellaneous Parts

The purpose of this memo is to aid design and to document values used. Any errors in these values will be reflected as errors in designed parts. Dimensions are taken from catalog sheets or from the parts to the accuracy of a vernier caliper. All dimensions are in inches.
Bushing for divider disk
Available from http://www.aircraftspruce.com/catalog/hapages/flangedbushings.php
Part FB1620-06 (Boston Gear part), Oilite bushing, $1.71
Diameter inside 1.000
Diameter outside 1.25
Diameter flange 1.50
Length body 0.75
Flange thickness 0.188
Bushing screw
Thread 4-48 UNF flat head socket cap screw
Body drill 0.120 (#31)
Tap drill 0.094 (#42)
Head diameter 0.25 nominal, C'sink angle 82° (41° off axis)
Length 0.625
O-ring for divider disk
Size -237, nominal OD 3.625, nominal cross-section diameter 0.125
Diameter inside 3.359±0.024
Diameter cross section 0.139±0.004
For face seals, groove depth is 0.123, very close to 0.125
Spark plug (e.g., Arnold SP-36 and SP-38)
Diameter threads 0.550 (14-1.25 mm) tapered seat
Seat taper 60° included angle (est.)
Diameter body 0.600 (est.)
Hex 0.625
OD plug socket 0.876
Diameter insulator 0.480
Diameter connector 0.260
Reach (thread depth from mounting face) 0.332
Projection (electrode below threads) 0.226
Length body 0.265
Length hex 0.172
Length shoulder 0.070
Length insulator 0.62
Length connector 0.35
Head nut
Internal thread 0.375-24 UNF
Hex 0.5625
OD socket 0.765
SAE flat washer, OD 0.8125, ID 0.406, thick 0.0625
Exhaust and transfer-passage screw
Thread 10-32 UNF
Head 0.312 dia by 0.190 high
Tap drill 0.159 (#21)
SAE flat washer, OD 0.500, ID 0.219, thick 0.049
Engine-mount screw
Thread 0.25-28 UNF
Head 0.375 dia by 0.250 high
Engine mount
Base extrusion is Z section, 1 ¼ x 2 x 1 ¼ x 3/16, part Z62032 from brunnerent.com. Need 36" (4 x 8" plus cutting margin)
Blow-off cage screw
Thread 8-36 UNF
Body drill 0.170 (#18)
Fuel injector
Consider illustrations on http://www.lindertech.com/reconinj.htm for a TBI injector.
Diameter body 0.75
Diameter nose 0.375
Length body 2.00
Length nose 0.375

Ron Schwiesow
18Feb11